| Block # | Total Block Area: |
| --- | --- |
| Impervious Surface | area in square meter (rounded to nearest 1 sq. m) | % of total block area (recorded to 1 decimal place) |
| Buildings | 12,215 m2 | 27.4% |
| Pavement - pedestrian | 2,797 m2 | 6.3% |
| Pavement - vehicles | 29,583 m2 | 66.3% |
| Total Impervious Surface | 44,595 m2 | 100% |
| Pervious Service | area in square meter (rounded to nearest 1 sq. m.) | % of total block area (recorded to 1 decimal place) |
| Gravel | 118.43 m2 | .4% |
| Grass | 27,160 m2 | 98.3% |
| Shrubs | 362 m2 | 1.3% |
| Total Pervious Surface | 27,640 m2 | 100% |
| Number of Large Trees: | approx. 121 large trees |

Example on how to find z-score of each surface:

| Category 1: Impervious Surface Area of Buildings |
| --- |
| Block # | % | Block # | % | Block # | % | Block # | % |
| 1 | 48 | 6 | 26 | 11 | 43 | 16 | 65 |
| 2 | 12 | 7 | 42 | 12 | 75 | 17 | 73 |
| 3 | 67 | 8 | 66 | 13 | 36 | 18 | 86 |
| 4 | 34 | 9 | 38 | 14 | 11 | 19 | 90 |
| 5 | 83 | 10 | 92 | 15 | 17 | 20 | 39 |

Mean 52.15     standard deviation 26.2

Example z-score for block #1: z1 = (52.15-48)/26.2 = 1.6

- Within each block number, we would multiply the z-score found for that block by the weighted values we assigned to each category, which would give us the Runoff Index (RI) for that block's surface.

  - Example: 1.6 x .006 =.0096, RI for block #1

- We would repeat these steps for each category (1-7) finding the RI for each block's surface.

- Next, we would add up all the block's total RI for each category to find the total runoff index for that area. This will allow us to find where on campus has the highest runoff problems.

- RI B#1 Buildings + RI B#1 Pedestrian + RI B#1 Vehicle + RI B#1 Gravel +RI B#1 Grass + RI B#1 Shrubs + RI #1 Trees = Total Runoff Index for Block #1